## Slide 1
Congestion & Flow Control of
Transmission in Space Segment
单乾

## Slide 2: Outline
Background
REFWA: Fair Congestion Control by Adjusting TCP Window Size
Congestion Control by Informing Neighbor Satellite to Reroute
  ELB: Routing-table-based Rerouting
  PAR & DRNL: Latitude-and-longitude-based Rerouting

## Slide 3: Background (1/1)
variance user density over the globe
differentiated services
  delay-sensitive vs. not sensitive
urban areas vs. rural areas vs. ocean
unbalanced traffic load
some satellites heavy loaded, while others idle

## Slide 4: REFWA (1/4)
Recursive, Explicit, and Fair Window Adjustment
key concept
  adaptively adjust TCP flow rate to available bandwidth
  intermediate satellites send feedback message to TCP source to adjust window size
  if feedback < RWND, then let RWND = feedback
source
destination
calculate feedback
(rewrite RWND in TCP)

## Slide 5: REFWA (2/4)
estimation of RTT and grouping
  a satellite estimate each flow’s RTT:
    Hb, Hf: backward & forward hop number when passing through this satellite
    ISLdelay: delay of inter-satellite link, assumed as a constant
  fairness: flows with the same RTT are grouped together
    the same RTT, the same feedback, then the same throughput
    vs. standard TCP: “undesirable bias against long RTT flows”
Notes: Hb Hf: TCP包的往返跳数 Hb+Hf+2即为链路总跳数
认为ISLdelay 是常数，且忽略了队列延迟
模拟显示这种估计方法的误差在30%~40%

## Slide 6: REFWA (3/4)
feedback computation
  at a certain satellite, for each link in k-th group, its feedback F during n-th time interval:
  recursive residual capacity of this link free queue size
  α, φ, ψ: parameters; : total TCP window size can be allocated
  RTTavg : average RTT of active links at n-th time interval & length of time interval

## Slide 7: REFWA (4/4)
experiments & conclusion (vs. TCP NewReno)
  measures: bottleneck link utilization, loss rate, queue size, fairness index
  for lower packet losses & smaller queue size, , ; for fairness, α=1
  more robust when abrupt change of traffic load happens
  fairness: operates correctly when there are links with variant RTTs (Fig b)
  multiple bottlenecks: doesn’t matter (Fig c)
  tolerant to errors in RTT estimate
Notes: robust: 使模拟中的连接数突然增加/减少，链路利用率、队列长度不会突然变化
fairness: 不同连接在考虑RTT的情况下，基本平分带宽

## Slide 8: ELB (1/3)
Explicit Load Balancing
key concept
  when a satellite is congested, it informs its neighbors to reroute
  packets should have passed this satellite are sent through alternative paths
  may cause out-of-order reception & packets have to traverse more hops
original path
congestion information
new path

## Slide 9: ELB (2/3)
three states of a certain satellite A
  α, β, χ are parameters
  β = 1 – p(packet dropping possibility); α = β / 2
  χ is relative to:
    traffic coming from the ground
    the satellite’s ability to output
    time we want the satellite to stay in normal state
name | total queue size | operation
free state | (0, α) | none
fairly busy state | [α, β] | send a warning message to neighbors, ordering them to start searching alternative paths
busy state | (β, +inf) | send a busy message to neighbors, ordering them to send only χ portion packets via A (e.g. flow control)
Notes: 关于χ：
首先计算当busy signal到达邻居时的队列长度
为了使之后的队列长度在时间θ内回到α以下，需要更新输入流量（输入流量既有来自邻居卫星的也有来自地面的，来自地面的流量是为不可调，只能调整邻居卫星传来的流量）
χ就是新输入流量与原有输入流量的比值

## Slide 10: ELB (3/3)
packet reordering recovery
  some packets traverse through shortest path,
  while others detour
  may cause TCP recovery
  solution: modify TCP code at receiver
  QUESTION1: what if topology changes
  and shortest link becomes longer?
  QUESTION2: what if alternative paths also congests?

## Slide 11: PAR & DRNL (1/4)
Priority-based Adaptive Routing & 基于邻居卫星负载状态的分布式路由算法
key concept:
  latitude-and-longitude-based
    the satellite has no routing table
    but a database recording satellites’ geographical location
  distributed
    a satellite decides the packet’s next hop merely
    according to link congestion conditions between two satellites

## Slide 12: PAR & DRNL (2/4)
routing strategy
  consider current satellite’s position & destination satellite’s position

## Slide 13: PAR & DRNL (3/4)
PAR’s priority metric of each link
  : successfully transmitted data per sec (past utilization)
  : average queue length, : dropped data per sec
  , , : parameters, set as 0.00005
  always select the link with smaller
PAR’s aging mechanism
  : current time unit; : aging period

## Slide 14: PAR & DRNL (4/4)
DRNL的链路负载状况 (vs ELB’s three states)
  认为4个方向的链路各自有队列
  B的综合链路利用状况
  A到B的链路利用率
  A到B的链路负载等级
  路由选择方法：
A
B
C
根据位置得出
的可选方向
if L(B) == L(C):
0.5概率选择B
0.5概率选择C
else if abs(L(B) - L(C)) == 1:
0.7概率选择负载等级低的卫星
0.3概率选择负载等级高的卫星
else:
0.85概率选择负载等级低的卫星
0.15概率选择负载等级高的卫星

## Slide 15
Thanks!