## Slide 1
引用了ELB的又2篇文献
单乾

## Slide 2: Outline
Background
DCCR: A Distributed Congestion Control Routing Protocol Based on Traffic Classification in LEO Satellite Networks
IADR: Dynamic Routing for Software-Defined LEO Satellite Networks based on ISL Attributes

## Slide 3: Background (1/2)
variance user density over the globe
differentiated services
  delay-sensitive vs. not sensitive
urban areas vs. rural areas vs. ocean
unbalanced traffic load
some satellites heavy loaded, while others idle

## Slide 4: Background (2/2)
name | total queue size | operation
free state | (0, α) | none
fairly busy state | [α, β] | send a warning message to neighbors, ordering them to start searching alternative paths
busy state | (β, +inf) | send a busy message to neighbors, ordering them to send only χ portion packets via A
ELB
  when a satellite is congested, it informs its neighbors to reroute
  three states of a certain satellite A:
original path
congestion information
new path
Notes: α β χ是参数，其具体值是计算得出

## Slide 5: DCCR (0/4)
A Distributed Congestion Control Routing Protocol Based on Traffic Classification in LEO Satellite Networks
  2021 IFIP/IEEE International Symposium on Integrated Network Management (IM)
  Laboratory of Networking and Switching Technology, Beijing University of Posts and Telecommunications

## Slide 6: DCCR (1/4)
key concepts
  distributed routing scheme: 9 different cases based on source & destination satellites’ location
  divide traffic into 3 types: according to the service’s sensitivity of latency & throughput
    improvement of ELB
  each satellite has 2 states: FREE & BUSY
    if queue length exceeds a threshold, the states turns from FREE to BUSY
    just like ELB

## Slide 7: DCCR (2/4)
routing scheme
position between source S & destination D |  | routing methods
different (latitude) positions, the same plane | - | along orbital plane
relative position, different planes | outside polar region | horizontally along intra-plane(?) ISL
 | in polar region | choose the node with higher latitude as next hop
different positions, different planes | in the same polar region | case 1
 | in different polar regions | case 2
 | S: outside polar region D: in polar region | case 3
 | S: in polar region D: outside polar region | case 4
 | … | case 5
 | … | case 6

## Slide 8: DCCR (3/4)
case 1
  S and D are in different positions & different planes
  S and D are in the same polar region
on the same side of the seam
on different sides of the seam

## Slide 9: DCCR (4/4)
traffic classification strategy
traffic allocation
  the routing scheme before increases the traffic on high-latitude satellites
  traffic B: select a low-latitude path with the same hop count as the shortest one
  traffic C: when the satellite is BUSY, some part of traffic C is allocated to detour
    just like ELB
traffic type | character | example service
traffic A | latency-sensitive, has the highest priority, shortest path should be guaranteed | voice over IP, interactive video application
traffic B | throughput-sensitive, should be transmitted with abundant bandwidth | video on demand, large file distribution
traffic C | ordinary traffic, do best to transmit | voice message, file transfer
Notes: 因为高纬度的轨间链路更短

## Slide 10: IADR (0/4)
Dynamic Routing for Software-Defined LEO Satellite Networks based on ISL Attributes
  2021 IEEE Global Communications Conference (GLOBECOM)
  Chongqing University of Posts and Telecommunications & University of Technology Sydney

## Slide 11: IADR (1/4)
key concepts
  software-defined satellite networks
  consider 3 ISL attributes to construct the link utility function
  use maximum deviation algorithm to adaptively calculate the weight of attribute parameters in link utility function
  use ISL utility to build path utility & choose the path with highest path utility

## Slide 12: IADR (2/4)
software-defined satellite networks
  control plane & data plane
  control plane:
    generates network topology snapshots
    calculates optimal routing paths
    needs to gather global information
  my understanding: a centralized routing algorithm
  how are satellite controllers distributed?

## Slide 13: IADR (3/4)
3 attributes for each ISL
  utility function of SNR of link (i, j) at any time t:
  utility function of link duration:
    : description is not clear in this paper, can be considered as how much remaining time the link can be maintained
    T: orbital period
  utility function of buffer queue:
    m: number of remaining packets at time t
    : number of packets reached in period t
    : number od packets processed by the satellite in time t
Notes: SNR: 换句话说就是链路通断信息

## Slide 14: IADR (4/4)
link utility
  , : weight of 3 attribute parameters
    + + =1
    calculated through an adaptive maximum deviation algorithm
      input: a reachable path, ISL decision attributes, link decision attribute utility
      output: ,
path utility
    : a candidate path : link utility value of link in
  select the path with the largest path utility

## Slide 15
Thanks!