## Slide 1: Inter-satellite Routing Algorithm Based on Local Information ——a unified framework
单乾
1

## Slide 2: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next
Notes: 联系年终总结的内容：先在OSPF的基础上修改

## Slide 3: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next

## Slide 4: Background
satellite network vs. terrestrial network
  high density
    star-link: 2,4000 satellites planned
    all satellites are considered as a SINGLE AS/area
  deterministic adjacencies
    a satellite communicates with 4 neighbors
    2 intra-orbit neighbors
    2 inter-orbit neighbors
  dynamic topology: intermittent ISLs
    while terrestrial networks are fixed
    due to movement of satellites
    may cause accidental link failures
    inter-orbit ISL periodically cut-downs
difficulties in maintaining link state
    in OSPF, each LSA will flood through the whole area: too much overhead
    however, topology can be predicted: no need to maintain all LSs
    research problem: how to take advantage of satellite network to maintain LSs with high efficiency & low cost?
polar ring
seam
orbit direction
ISL
Notes: 通常的研究是把整个卫星网络视为一个AS或者区域, 但也有研究致力于把卫星网络分区（如颜博的LPIH）
periodically cut-downs的原因：极区 运动 天线对准

## Slide 5: Background
predict network topology
  known orbit parameters
    calculate the position of any satellite at any time
  fixed adjacencies
    infer the link state of any ISL (according to the calculated position & fixed adjacencies)
    if a satellite not in polar ring, then it has all 4 ISLs
    if in polar ring, then it has only 2 intra-orbit ISLs
  calculated satellite position + inferred LS = predicted topo!
    not considering accidental link failures

## Slide 6: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next

## Slide 7: Main Idea
general link-state routing protocols (e.g. OSPF)
  neighbor discovering: Hello mechanism, parameter: hello interval
  neighbor relationship establishment: neighbor state machine
  link state advertisement: LSA flooding procedure, parameter: flood hop
  LSDB synchronization: upon receiving LSAs from other routers, each router updates its own LSDB with the newly received information
  shortest path calculation: each router applies a shortest path algorithm to build routing tables
  (advanced feature) load balancing: link load state is contained in protocol packets, which is determined by the length of forwarding queue
classic OSPF suits for terrestrial networks, but not satellite networks
  terrestrial: few link failures, the topology is fixed on the whole
  satellite: frequent link failures, may cause too much overhead for OSPF

## Slide 8: Main Idea
utilize the deterministic adjacencies of satellite networks
  not requiring LSDB synchronization
  advertise the time-varying LS more frequently to satellites in need
    based on cognition: only “nearby” LSs are more valuable to a satellite
  how to advertise the local info: flooding procedure
    a satellite floods LSAs of its directly connected ISL in an event-driven pattern
    range of flooding: hops (is a parameter)
  aim: reduce control overhead, while ensuring PDR and delay
assume
any satellite knows LS in hops and infers LS of other ISLs
decide next hop using
known & inferred LS

## Slide 9: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next

## Slide 10: Implementation
generation of random link failures
  definition 1. link failure rate : for a certain link, the expectation of its failure duration as a percentage of the total time duration
  definition 2. link failure duration : if a link fails at time , it will recover at , where is a constant value
  assumption 1. the link failure event follows the Poisson distribution, i.e. number of failure events per unit time
  according to def 1&2, the expectation of the number of failure events is
  note that link failures only happen when the link is working properly, i.e. we expect failures in time duration
  so we get
p
t
λ
link failure event series
input
input
randomly generate

## Slide 11: Implementation
limit the range of flooding: utilize the TTL field
  when a router / satellite generates a new LSA:
    when encapsulating as an LSU packet, set its TTL =
  when a router / satellite receives a newer & more recent LSA:
    origin OSPF:
    our method:
old LSU
TTL = 1
LSA
LSA
process
LSA
new LSU
TTL = 1
LSA
decapsulate
encapsulate
send
packet
old LSU
TTL =
LSA
LSA
process
LSA
new LSU
TTL =
LSA
decapsulate
send
packet
if > 1
if ≤ 1
do nothing
END

## Slide 12: Implementation
problem1: routing loops
  reason:
solution: new structure of routing table
  for each destination, we set (not 1) candidate RT entries
    : number of working links connected to this satellite
    when calculating SPT, set neighbors as the tree root respectively, then we get SPTs from 1 LSDB
  for each incoming packet, choose the least cost & not incoming interface as next hop
  avoid 2-satellite-loops (majority in loops), but can’t avoid 4/6/...-satellite-loops
9_5
10_5
11_5
11_4
9_5
10_5
11_5
11_4
original path
link failure happens
9_5
10_5
11_5
11_4
LSA floods regionally
I will recalculate my routing table, new next hop is 9_5
I didn’t receive LSA! My next hop remains 10_5
Notes: 在实验中观察到了震荡的现象，频率未知，而且传输成功率低似乎不全是由震荡导致

## Slide 13: Implementation
problem2: neighbor relationship establishment
  in Exchange state, one sends DD to its neighbor, describing its LSDB
  the other requests certain LSA to synchronize their LSDBs
  but in our method, synchronization is not expected!
  causes a long time during Loading
solution: mutable DD request
  after receiving DD, one only requests LSAs in hops, i.e. LSAs it “should know”
  or simply don’t request

## Slide 14: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next

## Slide 15: Experiment
experiment setup
  static “satellite” topology
    6 orbits, 11 satellites in each orbit
    “full connected”, i.e. each satellite has 4 links
  address space
    traditional IP
    each interface of an ISL has a unique IP
  network config
    between 2 satellites is a broadcast network
    link cost setup: according to propagation delay
simulation
  in 0~20s, run original OSPF
    simulate the prediction of topology
    ensure all satellites’ LSDB are synchronized at first
  in 20~120s, run our method
    a single delivery pair, sends UDP at 10pkt/s (ensures no congestion)
  performance metrics
    average packet loss
    average end to end delay
    control overhead
Notes: 介绍拓扑图 每条边的传播时延是按照真实情况计算得出的
目前只是简单实验，为了简便没有使用卫星的仿真环境，而是每个节点都固定

## Slide 16: Experiment: packet loss rate
control overhead & packet loss in different (???)
  large enough: OSPF
  each point is the average of 10 tests
  new routing table structure can optimize packet loss up to 80% (“loopAvoidance” vs. “noLoopAvoidance”)
  mutable DD request: less overhead, fluctuated loss rate
OSPF: overhead 0.65, loss 0.2%
Notes: 解释图表：每个点是相同的配置，在10个随机事件进行实验，取的平均值，每个点上的数字是LSA洪泛的跳数
横轴是整个网络的开销
四条线各自的含义
我们想找的是一个尽量靠左下角的点
相比原始OSPF，目前观测到的结果是可以减少90%的控制开销，同时保持和OSPF相近的传输成功率

## Slide 17: Outline
Background: characteristics of satellite network
Main idea of our local-information-based algorithm
Implementation of our method
Experiment setup & results
What’s next

## Slide 18: What’s next
confusion
  why there are so many fluctuations?
  observation: in 10 tests, only 1 or 2 tests have many packet losses, while others nearly zero packet loss. but why?
another possibly feasible loop avoidance
  based on TTL & Manhattan distance between current & dest satellites
change the static topology into osgEarth environment
  should add the function of topology prediction
more further: consider the load balance
  definition of “load”
  how to transmit load info between satellites
  what to do after receiving load info

## Slide 19: Thanks
19