## Slide 1
Routing in LEO Satellite Networks:
How Many Link-State Updates Do We Need?
单乾

## Slide 2: Contents
Background & motivation
Design considerations of link-state routing
Design of our LoFi
Performance evaluation

## Slide 3: Contents
Background & motivation
  Advantages & challenges of satellite networks
  Deterministic neighbor relationship in satellite networks
Design considerations of link-state routing
Design of our LoFi
Performance evaluation

## Slide 4: Background & motivation
Low earth orbit (LEO) satellite constellation
  Lower orbit altitude (500 ~ 2000km)
  Smaller satellite-ground latency (2~12ms)
  Each satellite has 4 inter-satellite links (ISL)
    4 neighbors
    2 in the same orbit, 2 in the adjoining orbits
Major challenge: unstable topology
  Relative movement between satellites
  Frequent ISL failure & recovery
    Regular: satellite move into / out of polar region
    Irregular: ISL breakdowns
ISL
Neighbor
To unleash the potential of large-scale LEO constellation,
efficient routing and forwarding is necessary
Satellite we focus on
Notes: 解释右图：参考文献中，不同规模的星座从DC到法兰克福的传播时延的CDF
c-latency: 光速 f-latency: 直线光缆的理论时延 Hib...：跨大西洋光缆 HFT: 高频交易 金融领域专线

## Slide 5: Background & motivation
Previous link-state routing protocols in satellite networks
  Mainly based on OSPF
  What to disseminate: coarse-grained link-states (connectivity of an ISL)
  How to disseminate: flood globally
  Ignore topology features of satellite networks
Topology feature: deterministic neighbor relationship
  Provides prior information about the topology
  Real-time connectivity of distant ISLs may not be that crucial
  A new opportunity to advertise localized fine-grained link-states
    Link connectivity & load
    Can achieve less control overhead and better delivery
Notes: 确定性邻居关系：Satellites know the existence of ISLs and other satellites, but do not know the connectivity

## Slide 6: Contents
Background & motivation
Design considerations of link-state routing
  Link-state update mechanism
    Semantics of link-states
    Method of link-state dissemination
    Trigger of link-state update
  Routing calculation mechanism
Design of our LoFi
Performance evaluation

## Slide 7: Design considerations of link-state routing
Link-state(LS) update mechanism: what/how/when to disseminate
  Semantics of LS
    A metric (bandwidth / delay / a predefined cost / …)
    An attribute (link type, e.g., p2p link, transit link…)
  Method of LS dissemination: a common way is flooding
    Normal flooding
    Lightweight flooding
  Trigger of LS update
Routing calculation
Link-state routing protocol
Link-state update
Routing calculation
Notes: A typical link-state routing protocol consists of a link-state update mechanism and a routing calculation mechanism. These two components must be properly designed to improve the content delivery performance and reduce the control overhead

## Slide 8: Design considerations of link-state routing
Link-state(LS) update mechanism: what/how/when to disseminate
  Semantics of LS
  Method of LS dissemination: a common way is flooding
    Normal flooding
    Lightweight flooding
  Trigger of LS update
Routing calculation
Link-state routing protocol
Link-state update
Routing calculation
LSU, TTL=1
LSU, TTL=1
LSU, TTL=1
LSU, TTL=1
For a constellation,
size of an LSU packet is ,
overhead of a flooding procedure is
Notes: 普通的flooding：每颗卫星收到LSU后，若认为该LSU中携带了最新的链路状态信息（通过序列号确定），都会向所有接口发送LSU报文（收到该LSU的那个接口除外）
会存在较多冗余传输

## Slide 9: Design considerations of link-state routing
Link-state update mechanism: what/how/when to disseminate
  Semantics of LS
  Method of LS dissemination: a common way is flooding
    Normal flooding
    Lightweight flooding
  Trigger of LS update
Routing calculation
Satellite that detects LS change and starts flooding
Calculated flooding topology
Overhead of a flooding procedure is theoretically
Link-state routing protocol
Link-state update
Routing calculation
Notes: Lightweight flooding 是22年的一篇文献提出的
在实现上，是个每颗卫星预先存好一个按时间切片的“洪泛拓扑”，这个拓扑是一个最小生成树，收到LSU了就沿这个洪泛拓扑转发
但是这种方法对链路故障比较敏感，而且计算、存储这个洪泛拓扑会引入额外的开销

## Slide 10: Design considerations of link-state routing
Link-state update mechanism: what/how/when to disseminate
  Semantics of LS
  Method of LS dissemination: a common way is flooding
    Normal flooding
    Lightweight flooding
  Trigger of LS update
    Event-triggered mode: disseminate LSU packets when detect link-state changes
    Time-triggered mode: monitor link-states periodically
Routing calculation
Link-state routing protocol
Link-state update
Routing calculation

## Slide 11: Design considerations of link-state routing
Link-state update mechanism: what/how/when to disseminate
Routing calculation mechanism
  Each satellite builds a graph based on its LSDB
  Calculate optimal routes to other satellites using the shortest path algorithm
  Each ISL is associated with a cost (i.e. semantics of link-states)
    A unit (representing one hop)
    Propagation delay
    Queuing delay
    A predefined value
    …
Link-state routing protocol
Link-state update
Routing calculation
Notes: Lightweight flooding 是22年的一篇文献提出的
在实现上，是个每颗卫星预先存好一个按时间切片的“洪泛拓扑”，这个拓扑是一个最小生成树，收到LSU了就沿这个洪泛拓扑转发
但是这种方法对链路故障比较敏感，而且计算、存储这个洪泛拓扑会引入额外的开销

## Slide 12: Contents
Background & motivation
Design considerations of link-state routing
Design of our LoFi (localized fine-grained link-state routing protocol)
  Key idea
    Reduce the dissemination range of coarse-grained link connectivity
    Incorporate fine-grained link-load awareness
  Parameters
    : the range of link-state dissemination
    : the sensitivity of load awareness
  Advantages: better delivery performance & smaller control overhead
Performance evaluation

## Slide 13: LoFi: overview
Link-state update mechanism
  Semantics of LS: link connectivity → link connectivity & link load
  Method of LS dissemination: global flooding → local dissemination
  Trigger of LS update: event-triggered
Routing calculation mechanism
  Link-state inference: utilizing deterministic neighbor relationship
  Considering both the shortest path and the backup path

## Slide 14: LoFi: link-state update
Semantics of link-states
  ISL connectivity & load (occupation ratio of the forwarding queue)
  Each LSU packet generated by a satellite contains state of 4 connected links
Method of link-state dissemination
  With deterministic neighbor relationship, there is no need for global flooding
  LoFi reduces the range of LS dissemination, parameterized by
  Disseminate LSU packets to satellites in hops by using the TTL field of LSU packets
LSU, TTL=
LSU, TTL=
LSU, TTL=
LSU, TTL=

## Slide 15: LoFi: link-state update
Trigger of link-state update
  Event-triggered mode
  Trigger1: link failure & recovery
  Trigger2: link load change, parameterized by
    Dissemination is triggered whenever
      : number of packets in forwarding queue
      : the load recorded in the last LSU message
      : maximal length of the forwarding queue
      : a parameter denotes the accuracy of detecting link load
    LSU packet contains:
    Smaller means more sensitive in load awareness

## Slide 16: LoFi: link-state update
An example when
LSU
LSU
LSU
LSU
LSU
LSU
The breakdown of link triggers LS update.
Satellite detects the LS change and generates an LSU packet:
TTL | LS ID | LS data | 
 |  | connectivity | load (occupation ratio)
1 |  | true | 0.6
 |  | true | 0.3
 |  | true | 0.24
 |  | false | --
TTL | LS ID | LS data | 
 |  | connectivity | load (occupation ratio)
1 |  | true | 0.6
 |  | true | 0.3
 |  | true | 0.24
 |  | false | --

## Slide 17: LoFi: link-state update
An example when
  can receive LSU packets generated by satellites within hops
  can obtain LS of green links
  Each satellite obtains link-states within hops far

## Slide 18: LoFi: routing calculation
ISL cost
  In LoFi, each ISL is associated with a link-cost metric
  & denotes the propagation & queuing delay
  Infer link-states out of the local dissemination range
    Using deterministic neighbor relationship (known existence of ISLs, but unknown link-states)
    Connectivity: thought as true
    Load: thought as 0
: distance between two satellites (calculated based on deterministic neighbor relationship)
: speed of light
: occupied length of forwarding queue (retrieved from LSU packets received)
: bandwidth

## Slide 19: LoFi: routing calculation
When receive a data packet, a satellite:
  Check the optimal outgoing interface
  If this interface is the packet came from, check the 2nd optimal interface
  If and only if there is no other interfaces, send this packet back to the incoming interface
Forwarding scheme: an example when
Note that Each satellite obtains link-states within hops far
  , don’t know is down
  But , , know
Calculated best route
Calculated 2nd best route
data
Due to localized LS dissemination,
satellites may not be able to directly calculate the optimal route,
but intermediate satellites can gradually correct it.

## Slide 20: Contents
Background & motivation
Design considerations of link-state routing
Design of our LoFi
Performance evaluation
  Experiment setup
  Light-load performance
  Heavy-load performance

## Slide 21: Performance evaluation
Experiment setup
  Packet-level simulation on inet 4.4
  Constellation: Iridium-like walker-star constellation, 760km, 6 * 11
  Bandwidth of ISL: 10Mbps data packet size: 1KB queue capacity: 1000packets
  Irregular ISL failures/recoveries: Poisson process
  Key metrics:
    Control overhead: transmission overhead caused by protocol control packets
    Data packet loss ratio
    End-to-end delay

## Slide 22: Performance evaluation: light load
  Transmission pair: randomly selected six-hop-far pairs
  Sending rate: 100pkt/s * 100s, ensures no congestion
  Baseline: OPSPF (OSPF + orbit calculation)
  Parameter setup
    Fix (i.e., no load awareness)
    Vary
    Test performance of LoFi under link failure rates
  Record overhead, loss ratio and delay under different s and link failure rates

## Slide 23: Performance evaluation: light load
Overhead, loss ratio and delay under different s and link failure rates
    Larger means more control overhead, but smaller packet loss ratio and smaller delay
    The marginal performance gain on packet delivery is nearly zero when
failure rate | parameter | performance | control overhead
5% | LoFi | almost same as OPSPF | 78% less
15% | LoFi | 3.9% more delay | 66% less
failure rate | parameter | performance | control overhead
5% |  | almost same as OPSPF | 78% less
15% |  | 3.9% more delay | 66% less

## Slide 24: Performance evaluation: heavy load
  Transmission pair: 4 pairs with overlapping ISLs
  Sending rate: 500pkt/s * 100s, the network is congested
  Baseline: OPSPF, ELB (a load balanced algorithm for LEO satellite networks)
  Parameter setup
    Fix link failure rate = 10%
    Vary
    Vary , i.e., with & without load awareness
  Record overhead, loss ratio and delay under different s and s

## Slide 25: Performance evaluation: heavy load
Overhead, loss ratio and delay under different s and s
    LoFisignificantly reduces packet loss ratio and delay than OPSPF & LoFi
      proves the effectiveness of load awareness in LoFi
    Packet delivery performance of LoFiincreases in .
    can almost harness all the benefit at the cost of small control overhead
    LoFi outperforms ELB in terms of load balancing
      Packet loss ratio: decreased by 94.4% delay: decreased by 67.6% overhead: decreased by 85.7%

## Slide 26: Performance evaluation: heavy load
LoFi vs. ELB under different link failure rates
  Vary , link failure rate
  As link failure rate increases, performance of all methods gets worse
  LoFi, LoFi both outperform ELB in all three metrics
  A larger means a smaller control overhead, but worse loss ratio and delay

## Slide 27: Conclusion & future works
Review the design of LoFi
  Localized fine-grained link-state routing for LEO satellite networks
  Key ideas
    Reduce the dissemination range of link-states
    Incorporate fine-grained link-load awareness
Packet-level simulations
  Light-load scenarios: outperforms OPSPF in terms of smaller control overhead
  Heavy-load scenarios: outperforms ELB in control overhead & performance
Future works
  Implement LoFi in our container-based emulator
  Try to further address forwarding loops & packet disorder issue

## Slide 28
Thanks!